## Slide 1: 5x5x5 LED Cube
Project By:
John Liang
Kohei Saito
Siva

## Slide 2: Table of Contents
LED Cube
  Cube Construction
  Base Construction
  IC Logic
  Ohms Law
  Code
XBee
  Configuration/ Initialization
  Sending/Receiving Data
  Closing Connection
Frequency Analysis
  Representation of sound on a computer and Fast Fourier Transforms
  Coding to analysis music

## Slide 3: Construction of Cube
A basic list of components:
150 LEDs
1 Perforated PC Board
22 Gauge wire
4 IC LS238 Chips, active High Output
30 NPN transistors (act as switches)
1 Arduino Uno
2 Xbee Series 1
1 Explorer for Xbee
1 Xbee shield for Arduino Uno

## Slide 4: Base Construction
4 pieces of 10” x 6” x 1” wood cut at 45° angle
1 piece of 7 ¾” x 7 ¾” x ¼” wood
1 piece of 8”x8” x ¾” wood
1 Can of rubberized spray paint

## Slide 5: PC Board Schematic

## Slide 6: LS238 Logic

## Slide 7: Transistor Logic

## Slide 8: Ohms Law
Ohm’s Law is I =
A Transposition of Ohm’s Law calculating for resistance is
Resistance was calculated for 1 LED even though there are 5 LED’s
The LED’s are rated for 20mA or 0.02Amps (The current)
= 250Ohm Resistance per column

## Slide 9: The Code
Must use the truth table from the LS238 chip
First LS238 chip’s output is determined by Pins 12, and 13 from the Arduino
Not using Pin Yo output to enable others, Using Pin for clear() method.
The LedOn(int led) method
  Turns the Led on for 1ms.
  Method of calculating corresponding column number for LED
    If the LED number is less than or equal to 25 just return the LED number
    If LED number is greater than 25
      Minus one from LED number and take the mod 25
  Method of calculating the corresponding row
    If LED number is less than or equal to 25 return layer zero
    If LED number is greater than 25, return LED number divided by 25.

## Slide 10: Xbee Configuration
Configuration
  Using 16 bit addressing for use of MYID for Xbee
    Meaning we can ignore the 64 bit addressing of Serial High, Serial Low
  Using MAC MODE 0
    MAC mode for 802.15.4 MAXSTREAM Header with acks
    Attempted use of no ACKS showed visible dropped packets
  Using PAN ID of 8888
  Using API Mode with PPP
    Provides three types of protocols
      Link Connection
      Authentication
      Network

## Slide 11: Xbee Sending/Receiving
Xbee Sender
  Set the 16 bit MYID to 1
  Sending one LED number at a time creates indiscernible patterns in lighting
  The sender must fill the 100 bytes of available memory space inside packet
  The 100 bytes of payload holds 50 integers or LED numbers
  The packet is sent even if all 5o slots of the LED array is not full if cycle ends
    A cycle is the processing of one sample of music. (Kohei will explain further)
Xbee Reciever
  MYID set to 2
  The Xbee receiver iterates through the payload array and calls the function of
  LedOn(int LED) and loops forever. (or at least till there is no power).

## Slide 12: Principle of the Sound
The principle of the sound is the “vibration” and we recognize sound by recognizing the vibration.
The “vibration” can be represented as the wave.
All sound have the volume, pitch, and frequency.
80Hz 1000Hz

## Slide 13: FFT Algorithm
FFT algorithm (Faster Fourier Transform) is the way to analyze the frequency.
It transforms signal in time domain (Sample Rate) into a signal in frequency domain.
In this algorithm it is impossible to calculate individual frequencies but calculate the frequencies of certain range.

## Slide 14: FFT Algorithm
Frequency at 1000Hz
Songs

## Slide 15: Sound API
Minim library is the Sound API for processing dealing with mp3, wav or other various file formats.
Basic Function (ddf.minim.*)
  AudioFile loadFile(String filename, int bufferSize)
  void play()
  void close() , void stop()
FFT Function (ddf.minim.analyze.*)
  abstract void forward(AudioBuffer buffer)
  int specSize()
  float getBandWidth(int i)
  float getBand(int i)

## Slide 16: Variables for FFT
Sampling Rate -> 44100Hz
  Default value of mp3
BufferSize -> 1024
  Default value for mp3
SpecSize -> BufferSize / 2 = 512
  Size will be half of buffer size due to FFT algorithm
BandWidth -> Sampling Rate/ BufferSize = 43.066406Hz
  Each block have the range of about 43Hz
  ex)
  Block 0: 0.0Hz ~ 43.066406Hz
  Block 1: 43.066406Hz ~ 86.13281Hz
  Block 2: 86.13281Hz ~ 129.19922Hz

## Slide 17: Divide Frequency into Low, Mid, High
Each frequency range have 4 setting variable.
Low Frequency
  lowStart: starting point of low frequency
  lowEnd: ending point of low frequency
  lowVol: volume filter for low frequency
  bplLow: blocks/LED for low frequency
Same variables for MID and HIGH
  ex) midStart, highStart

## Slide 18: Programming
int n = number of block
If: Start <= n <= End
for: int i; i >= bpl; i++
if: frequency volume > vol
return true
else
return false
Each line represent each band(block: 43.066406Hz)

## Slide 19: Example
AND HERE IS THE CUBE BEING DRIVEN BY MUSIC.